## Slide 1
THE PROBLEM
Why split a model at all
1 / 5
Five hospitals, one shared model; no member may hold it.
70B fp16 across 3 nodes: 47 GB per shard — fits nothing.
Across 16 nodes: 8.8 GB — fits an ordinary laptop.
Below ~13B this is theatre. The memory wall is the product.
Sovereign cloud IaaS, Europe: $12.6B in 2026, from $6.9B.
Gartner, 9 Feb 2026 (cited)
70B fp16, N=3
47.0 GB
70B fp16, N=8
17.6 GB
70B int4, N=3
11.8 GB
70B fp16, N=16
8.8 GB
16 GB laptop
24 GB 4090
80 GB H100 — off scale →
derived from Llama-3.3-70B config shapes — 70.552B params
Left of the 16 GB line, a room of ordinary laptops holds a frontier-class model. Right of it, they cannot — and quantization does not fix it: int4 of a 7B is still a 7B.
Notes: Open with the hospital sentence — a named buyer inside ten seconds, before any architecture. Then the chart, and be blunt about what it says: at half a billion parameters, splitting a model is theatre, and our own demo proves it by loading the whole thing on every node. The interesting line is the 16 GB one. Left of it, a room of ordinary laptops can hold a frontier-class model. Right of it, they cannot, and no amount of quantization fixes that — int4 of a 7B is still a 7B. That boundary is the entire product.

## Slide 2
WHAT RUNS TODAY
One token, three hops, today
2 / 5
Qwen2.5-0.5B, 24 layers, split 8/8/8 across three containers.
FastAPI nodes, CPU-only, 2 vCPU; gateway, coordinator, Prom, Grafana.
Node2 owns lm_head, so node2 is where a token is born.
Pipeline parallelism is not ours: GPipe 2019, Petals 2022.
What is new: the shard boundary is a trust boundary.
coordinator
node0
embed + L0–7 8.00 layer-eq
node1
L8–15 8.00 layer-eq
node2
L16–23 + norm + lm_head 17.13 layer-eq
token
[seq, 896] fp32 · base64 · JSON
client → gateway :8080 (api-key, circuit breaker) → coordinator :8081 → node0 → node1 → node2 → token
lm_head = 9.13 layer-equivalents
runs today — `docker compose up`. The "equal" 8/8/8 split really runs 8/8/17: 1.539x off balance on layer-equivalents, 1.30x measured wall clock (90-AUDIT F11).
Notes: This runs. Three containers, CPU only, no GPUs, and a real completion comes back. Say the prior art out loud before anyone asks: GPipe defined pipeline parallelism in 2019, Petals shipped it decentralized in 2022, and vLLM ships it today behind one flag. We did not invent the mechanism, and claiming we did is how you lose a technical judge in the first minute. What is different is that in all three of those, the shard boundary is a performance boundary. Here it is a trust boundary — and that changes what you build.

## Slide 3
THE ENGINEERING
Three bets: wire, bytes, queue
3 / 5
Wire: 8.483 → 0.089 ms per hop (reported, T1-A4).
4.0 ms/hop of that was TLS cert parsing on plain http (reported).
Bytes: bf16 halves the wire, 99.41% top-1, 3.5 µs (measured).
One channel is 972x the median — naive int8 outputs garbage (measured).
Queue: U = min(1, R/S). One request cannot fill three stages (derived).
A · WIRE
HTTP+JSON+b64 8.483 ms
DLP frame 0.089 ms
95x
40-byte header · persistent socket · TCP_NODELAY
B · BYTES
3584 B
fp32
1792 B
bf16
906 B
int8+outliers
✕
LAN crossover: ~2 Mbit/s — stop at bf16
C · QUEUE
R=1
33%
R=3
~100%
1.40 → 4.21 tok/s at unchanged per-request latency (modelled)
Panel B is a negative result we kept on the slide: below bf16 nothing pays until the link drops under ~2 Mbit/s (90-AUDIT F01 supersedes the team file here). Panel A is reported by T1-A4 and has no script in bench/ - reported, not reproduced here.
Notes: Three bets, and one of them is a negative result we kept on the slide. The wire: ninety-five times per hop, and the funny part is that four milliseconds of every hop was parsing X.509 certificates for a connection that never used TLS. The bytes: bf16 is free and we stop there, because we measured the crossover — below bf16 you only win under about two megabit. The queue is the one people miss: a single request cannot fill a pipeline, because token t+1 waits on token t. Only concurrency can, and three is the knee.

## Slide 4
THE SCOREBOARD
The scoreboard, and the caveats
4 / 5
1.27 → 24.2 tok/s, 19x, same three containers.
147,200 → 543 forwards/node: 271x redundant compute.
1,821.7 MB → 1.948 MB: 935x fewer bytes.
Caveat: bytes, not seconds. On a fast LAN we are compute-bound.
Caveat: v1 has never run as an integrated system.
V0
V1
FACTOR
TAG
bytes on the wire
1,821.7 MB
1.95 MB
935x
derived
redundant position-fwds
147,200
543
271x
derived
return path / token
607,744 B
4 B
151,936x
derived
throughput, R=3 balanced
1.27 tok/s
24.21 tok/s
19.0x
modelled
pipeline utilisation
33%
~100%
3x
derived
935x is wire bytes, not wall clock, and it is conservative: v0 star-routes, so the true figure is ~1,657x. 19x = 6.3x single-stream x 3.0x concurrency. Never run end-to-end.
Notes: The caveat is in the same size type as the numbers, on purpose. If I shrink it, you stop believing the table. Two-seventy-one-x is the number I would defend hardest — it is pure arithmetic on the model config, not a benchmark. Nine-hundred-thirty-five-x is the biggest number and the weakest claim, because it is bytes and on this LAN we are compute-bound; it wins on WAN, on one-gig ethernet, and at long context. Nineteen-x is modelled from stage times we measured on one laptop. We have not run v1 end to end. That is the honest state.

## Slide 5
THE HONEST CLOSE
The memory wall, and the ask
5 / 5
IS
✓
The option when weights exceed
the device you are allowed to use.
✓
70B int4, N=3 → 11.8 GB/shard
the memory wall, in one number.
✓
A trust boundary at the shard cut
not merely a performance boundary.
IS NOT
✕
Cheaper than an API
$5.76/day electricity vs $1.73/day of tokens (modelled).
✕
Encryption
~35% of tokens recoverable from an 8-layer activation (cited).
✕
True yet, in our own repo
node.py:36 loads the whole checkpoint today.
pre-sliced shards
v1, days
KV cache + local argmax
v1, days
binary bf16 frame
v1, days
reshard-on-failure
~63 net LOC
ASK
<FILL: pilot partner / judges' pick / compute credits>
Notes: I want to end on what this is not, because every line is a question you were going to ask. It is not cheaper than an API — a sixteen-node fleet burns five seventy-six a day in electricity to make a dollar seventy-three of tokens. It is not encryption; split inference raises the cost of recovering a prompt, it does not prevent it. And today every node still loads the whole checkpoint, which is forty lines from being false. What it is, is the only option when the weights do not fit the machine you are allowed to use.